Documentation for Simple7BotCtrl

Information
- the Code runs on an Arduino DUE
- the PWM Pins are: Pin 2,3,4,5,6,7,8,9
- the DUE receives 8 angles via the Serial Programming Port (next to the Powersupply connector)
- if the 8 angles are received correctly (all angles received) and at least one angle is different from the angles sent last time the DUE will set the PWM Signal corresponding to these Angles and then send ACK back
  - ACK is defined as 101
  - the angles sent by the other device (RPI or PC) can be 0° to 254°
    If the angle is 0° the number 1 should be sent by the RPI, for 45° -> number = 46, 254° number = 255 etc.
  - Even if only 1 angle is changed all angles must be sent!
  - If the same angles as last time are sent the DUE won't respond!
  - If something went wrong (less than 8 but more than 0 angles received) the DUE will respond with NACK (102)
  - Making sure that only allowed angles are sent is done by the RPI/PC!

Debug Mode: Disconnect Robot Arm first!

The Communication should be first tested on every new sending device!

Some Important Information will be sent to the Arduino Serial Monitor
Test communication and maybe also robot arm by sending stuff via the Serial monitor.
If the Robotarm is connected:
Send 8 bytes with chars corresponding to the values you want to set!
Sending 12345678 would set the values: 49, 50, 51, 52, 53, 54, 55, 56,
that means the angles 48°, 49°, 50°, 51°, 52°, 53°, 54°, 55° will be set!

Information Received by Serial Monitor in Debug Modus
ACK ("e")
- The executing Time
- The new and the last sent angles (new = "End Angle", last = "Start Angle")
- The "extra" Bytes sent by some Systems after the data bytes
  - if the extra Byte shows as nothing or 0 it means there is no extra Byte
    - if there is only 1 extra Byte set:
      #define REC_B_NUM 1
    - if there are no extra Bytes set:
      #define REC_B_NUM 0
To test for the Extra Bytes:
set: #define REC_B_NUM 2
send 8 bytes to the DUE via Serial and look at the response on the Serial Monitor.
If the extra Bytes are both 0 it means there are no extra bytes and REC_B_NUM should be set to 0.
Setting REC_B_NUM to a to high value will affect the receiving time because the Arduino will wait for a byte that is not coming, or even worse will think a databyte is a extra byte.
Setting REC_B_NUM to a to low value would write the extra bytes as an angle setting wrong angles.

Before Running the code for the first Time

1. Determine the number of Servos
2. Find out the start angles of the Servos
  1. where is the 0° Position?
  2. If the Servo can't move to 0° or 0° would be a bad Start angle, determine a Start angle that should be set.
3. Connect the Servos to Power and Signal.
Connect them in a order so that the Base Servo is on the DUE Pin 2, moving up the Arm the next Servo should be connected to Pin 3 etc. That makes sending the Angles easier.

Running the Code for the first Time

0. Disconnect the Robot Arm!
1. Open the Debug Code
2. set #define REC_B_NUM 2
3. define the numbers of Servos
4. set the PWM pins: const int pwmPins[NUM_SERVOS] = {2,3, ...};
5. Set the Start angles. (2.2 of Before running Code for the first Time)
6. run the debug mode to test the communication and check for extra bytes and to check if everything works as expected.
7. after setting REC_B_NUM to the right value the speed can be tested by sending:
123456788765432112345678876543211234567887654321
The first output for Executing time should be between 0 and 1000ms the following should be ~40ms.
If they are bigger than 1000ms check if REC_B_NUM has the rigth value.
By disabling the output of all the start and end angles the executing time will be 3ms.